## Slide 1: Instrument Transformers
By: Daniel Opoku

## Slide 2: INSTRUMENT TRANSFORMERS
Instrument transformers are used in connection with measurement of voltage, current, energy and power in ac circuits.
  To extend (multiply) the range of the measuring instrument
  To isolate the measuring instrument from a high-voltage line.
Direct measurement of High current and Voltage with conventional methods will compromise the operator safety.
Instrument transformers can be effectively used to step down the voltage and current within range of the existing measuring instruments of moderate size
  Current transformer or CT (extend current range)
  Voltage or potential transformers or PT (extend voltage range)

## Slide 3: INSTRUMENT TRANSFORMERS
Instrument transformers have their primary winding connected to the power line and secondary windings to the measuring instrument.
The measuring instruments are isolated from the high power lines.
Voltages in such cases may range from 11,000 to even 330,000 V.
  Measuring for metering as well as for relaying purposes.
It would be out of question to bring down these high-voltage lines directly to the metering board.
This will require huge insulation and pose great danger for operating personnel otherwise.
In such a case, instrument transformers can greatly solve this problem by stepping down the high voltage to safe levels for measurement.

## Slide 4: ADVANTAGES OF INSTRUMENT TRANSFORMERS
Shunt and multipliers used for extension of instrument ranges are suitable for dc circuits and to some extent, for low power, low accuracy ac circuits.
Advantages:
  Shunts cannot be used for circuits involving large current; otherwise the power loss in the shunt itself will become prohibitably high.
  Multipliers, once again, due to inherent leakage current, can introduce errors in measurement, and can also result in unnecessary heating due to power loss.
  Measuring circuits involving shunts or multipliers, being not electrically isolated from the power circuit, are not only safe for the operator, but also insulation requirements are exceedingly high in high-voltage measurement applications.
  Single range moderate size instruments can be used to cover a wide range of measurement, when used with a suitable multi-range CT or PT.

## Slide 5: CURRENT TRANSFORMERS (CT)
Primary winding in series with line currying the current to be measured.

## Slide 6: …that’s all… …thanks for your time…