## Slide 1: TE 271: Analog Communication Systems Lecture 4 Examiner: M. S. Ellis, PhD smellis.coe@knust.edu.gh 057 904 7591
September 27th , 2016

## Slide 2: Reference material
A. Yadav, “Analog Communication Systems”, University Science Press, New Delhi, 2008.
S. Sharma, “Communication Engineering”, First Ed., S.K. Kataria & Sons, New Delhi, 2011.
T. G. Thomas, “Analog Communication”, McGraw hill, New Delhi, 2007.

## Slide 3: Side Band Techniques
The equation for an AM wave is given by:
V = Vc cosωct + maVc/2 {cos(ωc + ωm)t + maVc/2 cos(ωc - ωm)t….….(10)
Purpose of modulation is to send the weak message signal with the help of a carrier, NOT to send the carrier
Now, the carrier can therefore be removed without affecting the net content of the information. This is known as suppressed carrier (SC)

## Slide 4
This will also require less power without affecting the net content of the information Proven below as;
By removing the carrier, 66.66% of the total power can be saved without affecting the net content of information

## Slide 6
REPRESENTATION OF AM-SC WAVE

## Slide 7
SPECTRUM OF AM-SC WAVE
Only positive freq for practical use

## Slide 8: Generation of DSB-SC
Methods of generation a suppressed carrier AM wave is the same as discussed in generation of an AM wave, i.e.
Linear Time Variant Circuit
Non-Linear Circuit
Similarly, an example of a linear time variant circuit for DSB-SC generation is a chopper circuit (also called switching circuit or ring modulator) ……. Refer from Lecture 3
Likewise, an example of a non-linear circuit used to generate DSB-SC is a balanced modular is used to generate…….. Refer from Lecture 3

## Slide 9
All diodes are in forward bias for positive half cycle of carrier signal. Therefore no signal across resistance R (input of BPF)
All diodes are in reverse bias so diodes acts as an open circuit. Therefore signal for negative cycle appears across resistance R (input of BPF)

## Slide 11
A balanced modulator (non-linear circuit) for DSB-SC modulation

## Slide 12: Demodulation of DSB-SC signal
Using Non-Linear Device
Using Linear Time-Variant Circuit

## Slide 13: Single Side-Band (SSB) Transmission
As discussed earlier under DSB-SC, there is really no need to transmit the carrier
By doing so we can save power and maintain the same bandwidth as in the case of AM
V = maVc/2 [cos (ωm+ωc) t * cos (ωc-ωm)t] ....DSB-SC wave
The DSB-SC wave contains two identical sidebands
There is really no need to transmit both side bands if only one can be used to transmit the information
V = Vc cos ωct + maVc/2 [cos (ωm+ωc) t * cos (ωc-ωm)t]

## Slide 14
By transmitting a single side band signal (SSB), 83.33 % of the total power has been saved
Transmission bandwidth requirement also drops by half
Reduced noise
Reduced fading
Applications where SSB is used include ??

## Slide 15: SSB Generation
DSB-SC Filtering Method: Since SSB modulation is the transmission of the upper or lower sideband, SSB can be generated by easily filtering the undesired side band of the DSB-SC signal
Filter should have bandwidth should equal to that of the message signal (not twice its bandwidth)
Center frequency of filter should equal to the center frequency of the desired side band (not carrier)
Setback: Filters with sharp edges do not exist. Non-sharp edges must be used.

## Slide 16
Phase-Shift Method: Here, the box marked -π/2 is a 90 degrees phase shifter that delays the phase of every frequency component by 90 degrees
At output XSSB(t) = m(t)cosωct ± m(t)sinωct
The difference represents LSB, and sum represents USB

## Slide 17: SSB Demodulation
The process for SSB demodulation is the same as that for a simple DSBSC demodulator.

## Slide 18: Vestigial