## Slide 1: Microprocessors
8-bit, 16bit and the Pentium processors

## Slide 2: 8- bit Microprocessors(8085)
8085, developed by intel is an 8-bit microprocessor.
It is a single chip designed using NMOS technology.
It is packaged in a 40 pin plastic DIP

## Slide 3: Features of 8085
It is an 8-bit microprocessor i.e., it can read, compute or output 8-bit data simultaneously.
It requires +5V (Vcc) and its ground is connected to Vss.
It can operate with 3MHz clock frequency
It has 16-bit address lines.
The lower 8-bit address bus(A0 –A7) and the data bus (D0 –D7) are multiplexed to reduced the number of external pin.
It has an 8-bit accumulator, and instruction register(IR), six 8-bit general purpose registers and two 16-bit registers.

## Slide 4: Data Bus and Address Bus
AD0 – AD7 : The 8-bit data bus is multiplexed with the lower half of the 16-bit address bus.
The remaining bits of the 16-bit address bus carry only addresses.

## Slide 5: Control Signals
The two control signals(RD and WR) identify the nature of the operation.
The ALE indicates the type of information currently being multiplexed on the address and data buses.
When ALE is high address information is on line AD0 – AD7
When ALE is low, these lines are being used for data transfer

## Slide 6: The 8086 Processor
It is a 16-bit microprocessor, meaning its ALU, GPRs and most of the instructions are designed to work with 16-bit binary words.
It has 16-bit address bus(can work with 1 MB of memory)
Each of the memory locations is 8-bit
It has 16 bit data bus
8086 has time multiplexed address and data bus
It requires 5MHz clock range.

## Slide 7: The Pentium Processor
Pentium is a brand used for a series of x86-compatible microprocessors produced by intel.
The name Pentium is originally from a Greek word pente meaning five(as the original Pentium processors used Intel's fifth-generation microarchitecture, the P5) and the latin ending –ium.
It includes some advanced features like virtualization and hyper-threading.

## Slide 8: The Pentium Processor
Produced by intel and it is packaged in 237-pin PGA
Pentium requires a +3.3 or +5.0v power supply for operation and its ground is connected to Vss.
The memory system of the Pentium is 4G bytes in size.
64-bit data bus width
System bus clock rate 60 or 66 MHz
Uses a superscalar architecture – instruction level parallelism

## Slide 9: The Pentium Processor
ZIF socket
Pin Grid Array(PGA)