## Slide 1: x86 Processor Architecture
TEXT2 (2.2-2.5)

## Slide 2: General microprocessor overview

## Slide 3: The Clock
Each operation involving the CPU and the system bus is synchronized by an internal clock pulsing at a constant rate.
The basic unit of time for machine instructions is a machine cycle (or clock cycle ).
The speed of oscillation of the clock is usually quoted per processor.
A 1GHz processor has a clock that oscillates 1 billion times per second.
The duration of a clock cycle is calculated as the reciprocal of the clock’s speed. (1ns for a 1GHz clock)

## Slide 4: x86 Processors
x86 processors have three primary modes of operation:
Protected Mode
  Protected mode is the native state of the processor, in which all instructions and features are available.
Real-Address Mode
  Real-address mode implements the programming environment of the Intel 8086 processor with a few extra features.
System Management Mode
  provides an operating system with a mechanism for implementing functions such as power management and system security.

## Slide 5: Basic x86 Program Registers
Registers are high-speed storage locations directly inside the CPU, designed to be accessed at much higher speed than conventional memory.
The general-purpose registers are primarily used for arithmetic and data movement.
Portions of some registers can be addressed as lower 16-bit or 8-bit values.
For example, the EAX register has a lower 16-bit AX part, while the AX register, has an 8-bit upper half named AH and an 8-bit lower half named AL.

## Slide 7
All ..X general purpose registers can be expressed in the same formats shown for EAX previously.
The remaining general-purpose registers can only be accessed using 32-bit or 16-bit names

## Slide 8: Special-purpose general-purpose registers
EAX: Used for multiplication and division instructions.
ECX: Used by the CPU as a counter in loop instructions (automatic)
ESP: Used to point to the stack
ESI and EDI: Used for high speed memory transfer instructions.
EBP: Points to a memory location on the stack. Usually used by high level languages.
The EIP: stores the address of the next instruction to be executed.

## Slide 9
EFLAGS: They indicate the condition of the microprocessor and control its operation.
Status flags: reflect the outcomes of arithmetic and logical operations performed by the CPU.
  Carry flag (CF): result is too large to fit into the destination (unsigned).
  Overflow flag (OF): result is too large or too small to fit into the destination (signed).
  Sign flag (SF): result is negative.
  Zero flag (ZF): result is zero.
  Auxiliary Carry flag (AC): a carry from bit 3 to bit 4 in an 8-bit operand.
  The Parity flag (PF): the least-significant byte in the result contains an even number of 1 bits.

## Slide 10: EFLAG register for x86 processors (up to Pentium)
Control Flags
I (Interrupt): controls interrupt request pin (INTR). If I=1 pin is enabled. If I=0, the pin is enabled. (Assembly: STI and CLI)
D (direction): Sets increment or decrement mode for DI and/or SI registers. D=1:automatic increment, D=2:automatic decrement. (Ass. STD and CLD)

## Slide 11: The Intel 8086

## Slide 12: 0
The Intel 8086 processor (1978) marked the beginning of the modern Intel architecture family.
Primary innovations: 16-bit registers, a 16-bit data bus and a segmented memory model permitting programs to address up to 1 MByte of RAM.
The original IBM PC contained the 8088, a slightly modified version of the 8086.
Backward Compatibility
Each processor introduced into the Intel family since the 8086 has been
backward-compatible with earlier processors.

## Slide 13: Real Address Mode
In real-address mode, an x86 processor can access 1,048,576 bytes of memory (1 MByte) using 20-bit addresses in the range 00000H to FFFFFH.
Intel engineers had to solve a basic problem: the 8086 had 16 bit registers.
They came up with a scheme known as segmented memory. All of memory is divided into 64-kilobyte (64-KByte) units called segments.

## Slide 14
Each segment begins at an address having a zero for its last hexadecimal digit.
To specify a particular byte address, the base address of its segment, as well as an offset is needed.
Hence addresses are in the form- segment:offset
The actual address is referred to as the physical, linear or effective address.

## Slide 15
The segment registers CS, DS, SS, ES, FS and GS are used for storing the base addresses of segments.
A typical program has three segments: code, data, and stack.
CS, DS and SS are used with these respectively.
ES, FS and GS may be used for ‘extra’ purposes.

## Slide 16: Protected Mode
Protected mode is the more powerful “native” processor mode.
When running in protected mode, a program’s linear address space is 4 GBytes, using addresses 0 to FFFFFFFF hexadecimal.
The flat segmentation model is appropriate for protected mode programming in MASM.
In the flat segmentation model, all segments are mapped to the entire 32-bit physical address space of the computer.
Segment registers point to segment descriptor tables, which the operating system uses to keep track of locations of individual program segments.

## Slide 17: Reminder
Download Visual Studio Express Edition for Assembly language programming.