## Slide 1: Digital Computer Design
VHDL (A First Look)

## Slide 2: Overview
Introduction
Basic Language Organization
Interface
Architecture Body
Logic Operators
Concurrency
Design Units and Libraries

## Slide 3: How We Approach VHDL
We’re interested in how to use VHDL
  Not so much concerned about the theory
  Examples are used to explain details
  Constructs presented in order of applicability
We need to learn the rules and practices
  Rules define how we must do things
    structure, keywords, etc.
  Practices are suggestions about how to do something
    indenting, capitalization, etc.

## Slide 4: Practices Used by the Author
Indenting:
  Statements embedded in other statements will be indented
Formatting:
  Keywords: lowercase and bold
  Identifiers: uppercase and standard weight
VHDL version:
  VHDL-87 primarily emphasized
  VHDL-93 features discussed where appropriate

## Slide 5: VHDL’s Organization
The basic VHDL model is known as a Design Entity and has two parts
  Interface - denoted by keyword entity
    defines I/O signals for the model
  Body - denoted by keyword architecture
    describes how the model works
Comments can help document either part
  Text after two dashes is part of a comment
  Comment ends at the end of line
  Must have -- on all comment lines

## Slide 6: VHDL Example
entity XOR2_OP is
-- Input/Output ports
port
(A, B : in BIT;
Z : out BIT);
end XOR2_OP;
architecture EXD of XOR2_OP is
-- declarations go before begin
begin
Z <= A xor B;
end EXD;
Interface
Body

## Slide 7: The Interface
Design
Entity
BODY
Interface
entity XOR2_OP is
-- Input/Output ports
port
(A, B : in BIT;
Z : out BIT);
end XOR2_OP;
Entity declaration
Port declaration

## Slide 8: Identifiers
Identifier construction rules:
  Can be of any length; any number of characters
    Tools have typical maximum of 255 characters
  Identifiers are NOT case sensitive
  Allowed characters are A-Z, a-z, _ (underscore)
  First character must be a letter
  Last character must not be an underscore
  Adjacent underscores are not allowed

## Slide 9: Port Definition
Port declarations are identified by the keyword ‘port’
  Define design entity input/output signals
  Declaration must specify:
    The name (identifier)
    The direction, defined by keywords in, out, inout, buffer, linkage
      We don’t use buffer or linkage
    The information type; predefined types are available
      BIT is predefined Boolean type with values of 0 & 1
      INTEGER is a signed type

## Slide 10: Port Definitions (cont.)
The port statement has the form of
  PORT ( signal definition clause(s) );
  where the I/O signal definitions are enclosed by parenthesis and followed by a semicolon
  Multiple signal definitions are allowed
    Definitions are separated by a semicolon
    There is no semicolon after the last definition
The port statement can span many lines

## Slide 11: The Body
Design
Entity
BODY
architecture EXD of XOR2_OP is
-- declarations go before begin
begin
Z <= A xor B;
end EXD;

## Slide 12: The Body (cont.)
The VHDL model body describes how the model works
  Separate from interface to allow for alternate implementations
  header begins with keyword ‘architecture’
    header identifier names the body
    also identifies the associated design entity interface
  Two distinct parts of body follow header
    Declarative part - variables, etc. defined
    Statement part - contains operational statements

## Slide 13: Body Structure
Architecture EXD of XOR2_OP is
--Make any declarations before the begin
-- Objects must be declared before use
begin
-- Put the operational statements here
end EXD;
Same identifier;
names the architecture
Identifies the
associated
interface

## Slide 14: Logic Operators
VHDL provides the following predefined basic logic operators:
Keyword
and
or
xor
xnor*
nand
nor
not
Definition
conjunction
inclusive or
exclusive or
complement exclusive or
complement conjunction
complement inclusive or
complement
* only predefined in VHDL-93

## Slide 15: Logic Operators (cont.)
Predefined operators are all binary except for ‘not’
Multi-input operators formed from series of binary operators
  AND-3: A and B and C
Expression evaluation differs from switching algebra
  and, or, nand, nor are ‘short-circuit’ operators
  right operand not evaluated if left operand determines result

## Slide 16: Operator Precedence
Unary ‘not’ has a higher precedence than any binary operator
ALL binary operators have the SAME precedence
Operators with the same precedence are evaluated left-to-right
Operators in parentheses are evaluated first; innermost to outermost order
  Must be used for proper AND - OR evaluation

## Slide 17: Body Signal Declarations
Similar to interface ‘port’ declaration
  must define identifier, type
  signals are internal to body; direction not needed
Keyword is ‘signal’; declared in declarations part of body
Equivalent to defining intermediate circuit signals for symbolic analysis
E.G.
signal INT1, INT2: BIT;

## Slide 18: Concurrency
Software source code statements execute in page order (i.e. sequential order)
VHDL concurrent signal assignments execute only when associated signal change value (i.e. concurrent order)
  page sequence has nothing to do with execution
  assignments are on a nonprocedural stimulus/ response basis
  signal assignments may trigger other concurrent assignments

## Slide 19: Concurrent Operation Example
entity XOR2_OP is
port
(A, B : in BIT;
Z : out BIT);
end XOR2_OP;
architecture AND_OR_CONC of XOR2_OP is
signal INT1, INT2: BIT;
begin
Z <= INT1 or INT2;
INT2 <= not A and B;
INT1 <= A and not B;
end AND_OR_CONC ;

## Slide 20: Design Units and Libraries
VHDL is defined such that more complex pieces are built from simpler pieces
Libraries
Design Units
Statements
Expressions
Objects
Types

## Slide 21: Design Units and Libraries (cont.)
VHDL model part that can be independently analyzed (error checked) is a design unit
  Primary Design Units
    Entity Declaration
    Package Declaration
    Configuration Declaration
  Secondary Design Units
    Architectural Body
    Package Body
  Primary units analyzed before secondary units

## Slide 22: Design Units and Libraries (cont.)
Two predefined libraries in VHDL
  STD - contains predefined VHDL constructs such as types, objects, etc.
  WORK - the working library
Many other libraries may exist as part of development environment
  IEEE library - standard types and operators needed for simulation and implementation
  User-defined libraries - designs for reuse
  Implementation specific libraries - logic families

## Slide 23: Dataflow VHDL
(Bit Vector Operations and Conditional Concurrent Signal Assignments)

## Slide 24: Outline
Vector types and declarations
Vector literal values
Vector operations
Slice reference and assignment
Conditional concurrent assignment
Relational operators
Selected assignment
Vector attributes

## Slide 25: Bit Vectors
Signals can be more than one bit (a vector)
  Represent P address and data, function selection, etc.
Declaration is similar to single bit signals
  Type is bit_vector or std_logic_vector
We also must specify vector index range and direction
  little endian: (low to high)
  big endian: (high downto low)

## Slide 26: Vector Declarations
port (
A, B: in std_logic_vector(7 downto 0);
Z: out std_logic_vector(1 to 16)
);
A and B:
Z:
1
2
3
4
5
6
7
8
9
7
6
5
4
3
2
1
0
10
11
12
13
14
15
16
Note! The first bit and last bit index numbers define the number of bits in the vector (i.e. max - min + 1)

## Slide 27: Vector Literals
Single bit binary literals are ‘0’ and ‘1’
Vector binary literals are “0101”, “10_01”
  literal values may have an underscore embedded to improve readability
For bit_vectors we can also specify values using octal, decimal, or hexadecimal.
  O”1234” D”1999” X”ABCD”
  NOTE: This doesn’t work for std_logic_vectors and the Xilinx tools (use function “to_std_logic_vector” to translate)

## Slide 28: Vector Logical Operations
Single bit logical operations also apply to vectors
  Operands MUST be the same size (generally applies to all vector operations)
  Assignment target must also have the same number of bits as the result
  Operations are applied bitwise to operands to produce the vector result

## Slide 29: Vector Operations
Given:
Signal A, B, Z: std_logic_vector(7 downto 0);
Then the following logical operation and assignment
Z <= A and B;
Is equivalent to:

## Slide 30: Vector Arithmetic Operations
Vector arithmetic operations are basically the same as vector logical operations
  Operands MUST be the same size
  Assignment target must also have the same number of bits as the result
  Operations are applied bitwise to operands to produce the vector result
The only difference is the carry or borrow
  Carry in/out must be specially handled
  Result can be 1 bit larger than operands (CO)

## Slide 31: 4 bit Adder (Data Flow VHDL)
entity add4 is
port (a, b: in std_logic_vector (3 downto 0);
cin: in std_logic; cout: out std_logic;
s: out std_logic_vector(3 downto 0)
);
end add4;
architecture df of add4 is
signal tmpsum std_logic_vector(4 downto 0);
begin
tmpsum <= (‘0’ & a) + (‘0’ & b) + (“0000” & ci);
s <= tmpsum(3 downto 0);
co <= tmpsum(4);
end df;

## Slide 32: Add4 Example
In the previous example note:
  The “&” symbol is the concatenation operator
    joins operands together so that result length is sum of lengths of operands.
  In order to be able to access the MSB carry out we had to add 5-bit values (used & operator to add leading zeros to operands)
  To assign result to S, we had to access only the least significant 4 bits of tmpsum; this is a SLICE
  The carry out is a single bit assignment of the MSB of the result

## Slide 33: Slice Reference and Assignment
A slice is a part of a vector
  accessed by a range clause
    (hi downto lo) or (lo to hi)
    indices cannot go out of bounds of original declaration
    range direction must be the same as the original vector
  a single index is used to access a single bit
    e.g. tmpsum(4);
  Assignee must be the same size as the slice
    co <= tmpsum(4);

## Slide 34: Conditional Concurrent Assignment
Up to now, signal assignment has been only based on evaluation of operand changes
  expressions are boolean algebra only
  hard to understand what is being implemented
E.G. 4 to 1 mux:
Z <= (a and not s(1) and not s(0)) or
(b and not s(1) and s(0)) or
(c and s(1) and not s(0)) or
(d and s(1) and s(0));

## Slide 35: Conditional Concurrent Assignment
General Form:
target_signal <= value1 when cond1 else
value2 when cond2 else
*
valuem when condm else
valuen;
Note that the condition clauses must evaluate to a logical expression.

## Slide 36: 4 to 1 Mux (Cond. Concurrent Form)
Z <= A when s = “00” else
B when s = “01” else
C when s = “10” else
D;
Note that in the last case, we did not specify a condition; this is the “when no other condition is met” case.
Note also that we can conditionalize the last case but if so, we must ensure that all possible condition combinations are addressed.

## Slide 37: Relational Operators
In the previous example we introduced a new operator, the relational “equals”
  The relational operators are
    = (equals) /= (not equal)
    > (greater than) < (less than)
    >= (greater or equal) <= (less or equal)
  Note that <= (less or equal) is same operator as <= (signal assignment); i.e. context dependent
  Precedence of relational operators is between “not” and the other logical operators.

## Slide 38: Select Signal Assignment
Another form of concurrent signal assignment is the Select assignment
  Similar to a software CASE statement
    we first identify the “discriminator” signal or expression we will test
    values and associated conditions are then identified
  Like conditional signal assignment we must ensure that all cases of discriminator are covered
    “others” condition makes this easy

## Slide 39: Select Signal Assignment
General Form:
WITH discriminator SELECT
target_signal <= value1 WHEN choices1,
value2 WHEN choices2,
*
valuem WHEN choicesm,
valuen WHEN others;
The “choices” are values of the discriminator; either single, multiple or a range.

## Slide 40: Select Signal Assignment
All possible values of the discriminator must be covered
  single value: when “0001”,
  multiple values: when “0100” | “0110” | “1000”,
  value range: when“1010” to “1111”,
  everything else: when others;
The last case “when others” must be the last clause if used
Comma separates clauses, semicolon ends the statement

## Slide 41: Select Signal Assignment
WITH digit SELECT
segs <= “1110111” when “0000”,
“0010010” when “0001”,
“1011101” when “0010”,
“1011011” when “0011”,
“0111010” when “0100”,
“1101011” when “0101”,
“0101111” when “0110”,
“1010010” when “0111”,
“1111111” when “1000”,
“1111010” when “1001”,
“1101101” when others;

## Slide 42: Vector Attributes
Attributes allow access to signal definition information
  useful when designing generic VHDL
  tells use range, index, length of a signal
General form is
  signal_name’attr_name
Some attributes are pre-defined

## Slide 43: Pre-defined Attributes
Name:
‘left
‘right
‘high
‘low
‘range
‘reverse_range
‘length
Definition
index value on left of range
index value on right of range
greatest index value of range
least index value of range
range expression of signal
reversed signal range expression
number of bits in range

## Slide 44: Pre-defined Attributes
Attribute
ex‘left
ex‘right
ex‘high
ex‘low
ex‘range
ex‘reverse_range
ex‘length
Value
11
8
11
8
(11 downto 8)
(8 to 11)
4
signal ex: std_logic_vector(11 downto 8);

## Slide 45: Defining Sequential Circuit Behavior

## Slide 46: VHDL Processes
VHDL process is the most common way to implement sequential circuits
  A process is a sequence of statements.
  Each process is a single concurrent statement.
  All processes in a design execute concurrently.
A process communicates with the rest of a design via signals or ports declared outside the process.
Processes can define either sequential OR combinational logic

## Slide 47: Process Statements
A process statement (or a process) implements a sequential algorithm
  Contains both sequential and concurrent statements
    Sequential statements are only used within a process
  Evaluation is sequential; i.e. top to bottom like software
    Multiple assignments to the same signal may exist
    The last assignment before the end of the process is the real assignment.

## Slide 48: Sequential Statements
The following are sequential statements.
  Assignment - assign values to variables and signals.
  Flow control - conditional execution (if and case), repeat (for...loop, while, until), and skip (next and exit).
  Subprograms - define sequential algorithms to use repeatedly in a design (procedure and function).
  Wait statements - describe a pause until an event occurs
  Null statements - declare that no action is necessary
Sequential statements MUST reside within a process

## Slide 49: Process Activation and Control
A process is activated when defined signals change state
  Monitored signals defined in sensitivity list
  Monitored signals listed in WAIT statements
Monitored signals are checked as part of architecture evaluation
  Any change of monitored signal activates the process.
  Process control statements determine which signal assignments will be performed.

## Slide 50: Processes with Sensitivity Lists
Processes can be defined with an explicit “sensitivity list”
  Sensitivity list is a list of signals that is monitored for changes
  Sensitive processes are activated when any of the sensitivity list signals change state
  A sensitivity list process cannot have wait statements defined within the process
    There is an implicit “WAIT ON” statement at the end of the process
    Process evaluation is suspended at the end of process.

## Slide 51: Processes without Sensitivity Lists
Processes can be defined without any sensitivity list
  These processes MUST have at least one WAIT statement.
    Some tools require WAIT to be the first statement after BEGIN.
    Initial process evaluation runs until first WAIT is encountered.
  The WAIT statement defines signals that are monitored for change.
  Non-sensitive processes are activated when WAIT statement signals change state
  Process suspends when next WAIT statement is encountered
    Some tools allow multiple WAIT statements per process.

## Slide 52: Process Evaluation
Once activated, process evaluation starts at point of last suspension.
  Processes execute top to bottom
  If no WAIT is hit before the end of process, evaluation loops back to the beginning and continues.
  Signal values referenced are those at process start.
  All signal assignments are only possible assignments.
  The last assignment before suspension is the assignment that will be performed
  ACTUAL SIGNAL ASSIGNMENTS ARE ONLY MADE AT THE END OF PROCESS EVALUATION!

## Slide 53: Process Structure
LABEL1: process (sensitivity list <optional>)
-- declarations
begin
--process statements like
--wait on CLK, RESET;
--wait until CLK'event and CLK='1';
end process;

## Slide 54: Variables
Variables are only declared within a process
  Used for loop counters, temp storage, etc.
  Scope is only within the process
  Form is same as signal except for “VARIABLE” keyword
Variable assignment -
  Form is vname := expression;
  Assignment takes effect immediately

## Slide 55: WAIT Statements
WAIT on sig1, sig2, …sign;
WAIT until condition;
WAIT for timeperiod;
Wait for event on one or
more of signals
Wait until condition is true
Wait for time to elapse

## Slide 56: WAIT Statements
Wait statements can be placed anywhere in process block
  execution proceeds until wait is encountered
  execution then suspends until wait is satisfied
A process may have multiple wait statements
Exception: Process with sensitivity list cannot contain any WAIT statements!
There may be tool-related limitations; most tools do not
fully implement all process relate VHDL features

## Slide 57: Conditional Process Execution
Process execution is in-line, top to bottom unless a conditional execution statement(s) is encountered
Types are similar to software constructs
  CASE
  IF THEN ELSE
Tools may not implement all forms

## Slide 58: CASE
case <expression> is
when choice1 => seq. Statements 1
when choice2 => seq. Statements 2
*
*
when others => seq. Statements others
end case;
Like the select assignment, the choices may be a single value,a group (c1 | c2 | c3) or a range (c1 to c3)

## Slide 59: IF THEN ELSE
If <condition> then
seq. Statements
elsif <condition> then
seq. Statements
else
seq. Statements
end if;
If a condition is true the associated statements are executed and the rest of the group are skipped.
NOTE: the “else if” case is
ELSIF (one word, e missing)

## Slide 60: Process Iteration
Allows repetitive execution (looping)
Three basic forms
  loop … end loop; (infinite)
  for <var in range> loop … end loop;
  while <condition> loop … end loop;
all may have an option label as prefix

## Slide 61: NEXT
Used to terminate current pass through loop
Four forms
  next; (absolute)
  next when <condition>;
  next label;
  next label when <condition>;
The last two forms allow termination to the end of an outer loop

## Slide 62: EXIT
Used to terminate entire loop execution
Four forms
  exit; (absolute)
  exit when <condition>;
  exit label;
  exit label when <condition>;
The last two forms allow termination from an inner loop to the end of an outer loop

## Slide 63: Combinational Logic Definition w/ Processes
Processes can define combinational logic functions
  ALL signals on the right side of assignment operator “<=“ MUST be listed in the process sensitivity list
  ALL input signal value combinations MUST be addressed (i.e. signal assignments defined)
  ALL output signals MUST be assigned values for all input combinations
Failure to meet the above conditions results in implied memory!

## Slide 64: Combinational Logic Processes (cont.)
The most common problem with defining combination logic process is meeting condition 2.
  An undefined input combination implies outputs don’t change; i.e. memory is needed.
  IF, END IF statement is the greatest culprit; there must be a “default” assignment.
    ELSE, when others, mainly used.

## Slide 65: Clock Edge Detection
You cannot just conditionalize behavior by detecting “clk = ‘1’; we need the clock edge
  Signal attribute ‘event is used
  clk’event is true just after a clk change; false the rest of the time
The combination of clk’event and value defines positive or negative clock edge
  Positive: (clk’event and clk = ‘1’)
  Negative: (clk’event and clk = ‘0’)

## Slide 66: Simple Decade Counter Example
Architecture behave of deccnt is
signal cntval: std_logic_vector(3 downto 0);
cntr: process (clk, reset)
begin
if (reset = ‘1’) then
cntval <= “0000”;
elsif (clk’event and clk = ‘1’) then
cntval <= cntval + “0001”;
if (cntval >= “1001”) then
cntval <= “0000”;
end if;
end if;
end process;
end behave;

## Slide 67: Enumerated Type Definition
You can define your own enumerated data types
  Handy when defining states and transitions
  Form is:
    TYPE type_name IS (value list);
Once declared, the data type is used to define new signals of that type

## Slide 68: Enumerated Type Example
type state_type is (reset, sync, load, out);
signal pstate: state_type;
ss: process (clk)
begin
if (clk’event and clk = ‘1’) then
case pstate is
when reset => ….
when sync => ….
etc.
end if;
end process;

## Slide 69: Sequential State Machines in VHDL
The two basic techniques are:
  The 3-process definition method
    State register process, next-state combinational logic process, output combinational logic process
  The 1-process and concurrent assignment method
    A single process defines state register and transitions
    Conditional or selected concurrent assignment define the output combinational logic

## Slide 70: Real-Time State Machine Example
type state_type is (idle, init, dat, par, stop);
signal pstate: state_type;
signal baud, last: std_logic;
signal clkdiv, cntr: integer range 0 to 100000000;
begin
cd: process (clk)
begin
if (clk’event and clk = ‘0’) then
clkdiv <= clkdiv + 1;
baud <= ‘0’;
if (clkdiv >= baudiv) then
clkdiv <= 0;
baud <= ‘1’;
end if;
end if;
end process;

## Slide 71: Real-Time State Machine Example (cont.)
cu: process (clk, reset)
begin
if (reset = ‘1’) then
pstate <= idle;
elsif (clk’event and clk = ‘1’ and baud = ‘1’) then
case pstate is
when idle =>
if (go = ‘1’) then
pstate <= init;
endif;
when init =>
pstate <= dat;

## Slide 72: Real-Time State Machine Example (cont.)
when dat =>
if (last = ‘1’ and pe = ‘1’) then
pstate <= par;
elsif (last = ‘1’ and pe = ‘0’ and ns = ‘1’) then
pstate <= stop;
elsif (last = ‘1’ and pe = ‘0’ and ns = ‘0’) then
pstate <= idle;
end if;
when par =>
if (ns = ‘1’) then
pstate <= stop;
else
pstate <= idle;
end if;

## Slide 73: Real-Time State Machine Example (cont.)
when stop =>
pstate <= idle;
end case;
end if;
end process;
cp: process (clk)
variable lodval: integer range (0 to 7);
begin
if (clk’event and clk = ‘1’) then
if (pstate = dat) then
cntr <= cntr – 1;

## Slide 74: Real-Time State Machine Example (cont.)
else
lodval := 4;
if (ls(0) = ‘1’) then lodval := lodval + 1; end if;
if (ls(1) = ‘1’) then lodval := lodval + 2; end if;
cntr <= lodval;
end if;
end if;
end process;
last <= ‘1’ when (cntr = “000”) else ‘0’;
mark <= ‘1’ when (pstate = idle or pstate = stop) else ‘0’;
space <= ‘1’ when (pstate = init) else ‘0’;
dout <= ‘1’ when (pstate = dat) else ‘0’;
pout <= ‘1’ when (pstate = par) else ‘0’;

## Slide 75: Structural Modeling in VHDL

## Slide 76: Overview
Component and signal declarations
Component instantiations
Hierarchical structures
Packages
Name spaces and scope

## Slide 77: Schematic Vs. VHDL
Structural VHDL models the structure of a circuit; similar to circuit schematic
  Defines the circuit components
  Describes how components are connected
System behavior or functionality is indirectly defined; model only lets components work in a certain, defined way.
  Symbolic analysis allows us to determine functionality of system from understanding component behaviors

## Slide 78: Example Schematic
A_IN
B_IN
C_IN
Z_OUT
INT1
INT2
INT3
A
B
Z
Z
B
A
C
A
B
Z
A
B
Z
A1
A2
A3
O1

## Slide 79: Example Structural VHDL Interface
-- Define the Interface
entity MAJORITY is
  port
    (A_IN, B_IN, C_IN: in BIT;
    Z_OUT : out BIT);
end MAJORITY;

## Slide 80: Example VHDL Body
architecture STRUCTURE of MAJORITY is
-- Declaration of components and local signals
  component AND2_OP
    port (A, B : in BIT; Z : out BIT);
  end component;
  component OR3_OP
    port (A, B, C : in BIT; Z : out BIT);
  end component;
  signal INT1, INT2, INT3 : BIT;

## Slide 81: Example VHDL Statement Part
begin
  -- Define the component connections
  A1: AND2_OP port map (A_IN, B_IN, INT1);
  A2: AND2_OP port map (A_IN, C_IN, INT2);
  A3: AND2_OP port map (B_IN, C_IN, INT3);
  O1: OR3_OP port map (INT1, INT2, INT3, Z_OUT);
end STRUCTURE;

## Slide 82: Design Entity – Component Relationship
OR3_OP
AND2_OP
A1
A2
A3
O1
Design entities
Components
Instantiations
OR3_OP
AND2_OP

## Slide 83: Component Declarations
Component declarations reference the components that are to be connected
  Identified by keyword ‘component’
    Definition terminated by ‘end component’
  Port statement define the interface
    Identifier, direction, type same as in port statement in design entity interface definition
  Component to entity association is defined by a ‘configuration’
    Default configuration associates components and entities that have the same interface

## Slide 84: Signal Declarations
Instantiated components need connecting; signals do this
  Effectively form the internal gate-to-gate wiring
  Keyword is ‘signal’
  Must specify identifier(s) and type

## Slide 85: Component Instantiation Statements
Component instantiation statements define specific, names instances of components
  Prefaced with a label: identifier (names the part)
  Followed by the component name
  Followed by keyword ‘port map’
  Followed by signal map list
    Associates signals with component interface entity
    Connectivity is either positional association or named association

## Slide 86: Port Map Associations
Positional association connects port identifiers to port map identifiers in order of occurrence
Named association explicitly identifies the connection between port identifiers and port map identifiers
  Association is “port name => signal name”
  Associations can appear in any order
Both associations can appear in one port map
  Positional before named

## Slide 87: Positional Port Map Association
In our example, the AND gate port signal declarations were A, B, and Z in that order
The positional association connects comp. Input A to A_IN, B to B_IN, and output Z to INT1
A1: AND2_OP port map (A_IN, B_IN, INT1);

## Slide 88: Named Port Map Association
Now let’s change the component instantiation to use named association as follows.
Note that this gives us exactly the same connections as before but they can be listed in any order
A1: AND2_OP port map (Z=>INT1, B=>B_IN, A=>A_IN);

## Slide 89: Hierarchical Structures
Design entity definitions are referenced as components
Components are instantiated to form new design entities
VHDL promotes reuse through hierarchical structures

## Slide 90: Hierarchical Structure Diagram

## Slide 91: Packages
Multiple VHDL model descriptions tend to use the same component declarations, etc.
  Lots of wasted effort to repeat declarations
  Good opportunities for mistakes
Packages provide a method for collecting common declarations in a central location
Package declarations can then be reused by referencing the package via ‘use’ statement
E.G. Use WORK.LOGIC_OPS.All;

## Slide 92: Package Definition Example
package LOGIC_OPS is
  component AND2_OP
    port (A, B: in BIT; Z: out BIT);
  end component;
  component OR2_OP
    port (A, B: in BIT; Z: out BIT);
  end component;
  component NOT_OP
    port (A: in BIT; Z: out BIT);
  end component;
end LOGIC_OPS;

## Slide 93: Example of Package Usage
entity XOR2_OP is
  port (A, B: in BIT; Z: out BIT);
end XOR2_OP;
use WORK.LOGIC_OPS.all
architecture STRUCT of XOR2_OP is
  signal ABAR, BBAR, I1, I2: BIT;
begin
  N1: NOT_OP port map (A, ABAR);
  N2: NOT_OP port map (B, BBAR);
  A1: AND2_OP port map (A, BBAR, I1);
  A2: AND2_OP port map (B, ABAR, I2);
  O1: OR2_OP port map (I1, I2, Z);
end STRUCT;
Library
Package

## Slide 94: Name Spaces and Scope
Scope defines the extent or region of applicability of a declaration
  Also known as the name space of a declaration; where the declaration’s identifier is valid
Any declaration in a design entity is valid in the entity and associated architectures
  Identifiers defined in the interface are valid in the associated body

## Slide 95: Use Clauses and Packages
Identifiers declared within a package are valid in the enclosing package
Scope of package declaration is extended to other parts of a VHDL model by use clause
  If before entity statement, all declarations are available to both entity and architecture
  Use clause can also occur before package declaration
    Packages can access other packages via use clause
    Hierarchy of packages can be constructed

## Slide 96: Package Export Types
Packages can make visible or export three levels of declarations
  1) The package name
  2) A subset of the package declarations
  3) all package declarations
Export type is specified by the suffix of the package identifier in use clause
  So far we seen case 3; .All

## Slide 97: Package Exports - Name Only
Name only export (no suffix):
  E.G. Use WORK.LOGIC_OPS;
In this case component instantiations must be specified by both package AND component
  E.G. A1: LOGIC_OPS.AND2_OP port map ....
This lets us access a specific component definition with the same name as another

## Slide 98: Package Exports - Explicit Reference
An explicit list of component package declarations may also be constructed
  E.G. Use WORK.LOGIC_OPS.AND2_OP,
  Work.Logic_ops.Or2_op;
Individual components are listed in use clause separated by commas
Technique limits the declarations visible in a name space

## Slide 99: Nested Scope
Like strongly type SW languages, VHDL scopes can be nested
VHDL follows the standard nested scope rules for name space visibility
  Inner-level declarations not visible to outer-levels
  Outer-level declarations are visible to inner-levels
  Inner-level declaration with same name as outer-level declaration overrides outer-level declarations

## Slide 100: Library Clauses
A library clause declares the name of a library
  E.G. Library WORK, STD;
  Use STD.STANDARD.All;
Predefined libraries are WORK and STD
  Above declarations are part of all design units
User-defined libraries or development tool libraries MUST be declared
  A package may include library declarations