## Slide 1: Digital Computer Design
Tabular Minimization (Quine-McCluskey)

## Slide 2: Quine-McCluskey (Tabular) Minimization
Two step process utilizing tabular listings to:
  Identify prime implicants (implicant tables)
  Identify minimal cover (cover tables)
All work is done in tabular form
  Number of variables is not a limitation
  Basis for many computer implementations
  Don’t cares are easily handled
Proper organization and term identification are key factors for correct results

## Slide 3: Quine-McCluskey Minimization (cont.)
Terms are initially listed one per line in groups
  Each group contains terms with the same number of true and complemented variables
  Terms are listed in numerical order within group
Terms and implicants are identified using one of three common notations
  full variable form
  cellular form
  1,0,- form

## Slide 4: Notation Forms
Full variable form - variables and complements in algebraic form
  hard to identify when adjacency applies
  very easy to make mistakes
Cellular form - terms are identified by their decimal index value
  Easy to tell when adjacency applies; indexes must differ by power of two (one bit)
  Implicants identified by term nos. separated by comma; differing bit pos. in () following terms

## Slide 5: Notation Forms (cont.)
1,0,- form - terms are identified by their binary index value
  Easier to translate to/from full variable form
  Easy to identify when adjacency applies, one bit is different
  - shows variable(s) dropped when adjacency is used
Different forms may be mixed during the minimization

## Slide 6: Example of Different Notations
F(A, B, C, D) =  m(4,5,6,8,10,13)
1 ABCD 4 0100
ABCD 8 1000
2 ABCD 5 0101
ABCD 6 0110
ABCD 10 1010
3 ABCD 13 1101
Full variable Cellular 1,0,-

## Slide 7: Implication Table (1,0,-)
Quine-McCluskey Method
  Tabular method to systematically find all prime implicants
  ƒ(A,B,C,D) = Σ m(4,5,6,8,9, 10,13) + Σ d(0,7,15)
  Part 1: Find all prime implicants
  Step 1: Fill Column 1 with active-set and DC-set minterm indices. Group by number of true variables (# of 1’s).
Implication Table
Column I
0000
0100
1000
0101
0110
1001
1010
0111
1101
1111
NOTE: DCs are included in this step!

## Slide 8: Implication Table (cellular)
Quine-McCluskey Method
  Tabular method to systematically find all prime implicants
  ƒ(A,B,C,D) = Σ m(4,5,6,8,9, 10,13) + Σ d(0,7,15)
  Part 1: Find all prime implicants
  Step 1: Fill Column 1 with active-set and DC-set minterm indices. Group by number of true variables (# of 1’s).
Implication Table
Column I
0
4
8
5
6
9
10
7
13
15
NOTE: DCs are included in this step!

## Slide 9: Minimization - First Pass (1,0,-)
Quine-McCluskey Method
  Tabular method to systematically find all prime implicants
  ƒ(A,B,C,D) = Σ m(4,5,6,8,9,10,13) + Σ d(0,7,15)
  Part 1: Find all prime implicants
  Step 2: Apply Adjacency - Compare elements of group with N 1's against those with N+1 1's. One bit difference implies adjacent. Eliminate variable and place in next column.
  E.g., 0000 vs. 0100 yields 0-00
  0000 vs. 1000 yields -000
  When used in a combination, mark with a check. If cannot be combined, mark with a star. These are the prime implicants.
  Repeat until nothing left.
Implication Table
Column I
0000 
0100 
1000 
0101 
0110 
1001 
1010 
0111 
1101 
1111 
Column II
0-00
-000
010-
01-0
100-
10-0
01-1
-101
011-
1-01
-111
11-1

## Slide 10: Minimization - First Pass (cellular)
Quine-McCluskey Method
  Tabular method to systematically find all prime implicants
  ƒ(A,B,C,D) = Σ m(4,5,6,8,9,10,13) + Σ d(0,7,15)
  Part 1: Find all prime implicants
  Step 2: Apply Adjacency - Compare elements of group with N 1's against those with N+1 1's. One bit difference implies adjacent. Eliminate variable and place in next column.
  E.g., 0000 vs. 0100 yields 0-00
  0000 vs. 1000 yields -000
  When used in a combination, mark with a check. If cannot be combined, mark with a star. These are the prime implicants.
  Repeat until nothing left.
Implication Table
Column I
0 
4 
8 
5 
6 
9 
10 
7 
13 
15 
Column II
0,4(4)
0,8(8)
4,5(1)
4,6(2)
8,9(1)
8,10(2)
5,7(2)
5,13(8)
6,7(1)
9,13(4)
7,15(8)
13,15(2)

## Slide 11: Minimization - Second Pass (1,0,-)
Implication Table
Column I
0000 
0100 
1000 
0101 
0110 
1001 
1010 
0111 
1101 
1111 
Column II
0-00 *
-000 *
010- 
01-0 
100- *
10-0 *
01-1 
-101 
011- 
1-01 *
-111 
11-1 
Column III
01-- *
-1-1 *
Quine-McCluskey Method
  Step 2 cont.: Apply Adjacency - Compare elements of group with N 1's against those with N+1 1's. One bit difference implies adjacent. Eliminate variable and place in next column.
  E.g., 0000 vs. 0100 yields 0-00
  0000 vs. 1000 yields -000
  When used in a combination, mark with a check. If cannot be combined, mark with a star. These are the prime implicants.
  Repeat until nothing left.

## Slide 12: Minimization - Second Pass (cellular)
Quine-McCluskey Method
  Step 2 cont.: Apply Adjacency - Compare elements of group with N 1's against those with N+1 1's. One bit difference implies adjacent. Eliminate variable and place in next column.
  E.g., 0000 vs. 0100 yields 0-00
  0000 vs. 1000 yields -000
  When used in a combination, mark with a check. If cannot be combined, mark with a star. These are the prime implicants.
  Repeat until nothing left.
Implication Table
Column I
0 
4 
8 
5 
6 
9 
10 
7 
13 
15 
Column II
0,4(4) *
0,8(8) *
4,5(1) 
4,6(2) 
8,9(1) *
8,10(2) *
5,7(2) 
5,13(8) 
6,7(1) 
9,13(4) *
7,15(8) 
13,15(2) 
Column III
4,5,6,7(3) *
5,7,13,15 (10) *

## Slide 13: Prime Implicants
Prime Implicants:
X
1
0
1
0
1
1
1
0
X
X
0
0
1
0
1
AB
00
01
11
01
11
10
C
CD
A
D
B
00
10

## Slide 14: Prime Implicants (cont.)
Stage 2: find smallest set of prime implicants that cover the active-set
recall that essential prime implicants must be in final expression
Prime Implicants:
X
1
0
1
0
1
1
1
0
X
X
0
0
1
0
1
AB
00
01
11
01
11
10
C
CD
A
D
B
00
10

## Slide 15: Coverage Table
rows = prime implicants
columns = ON-set elements
place an "X" if ON-set element is
covered by the prime implicant
Coverage Chart
0,4(0-00)
0,8(-000)
8,9(100-)
8,10(10-0)
9,13(1-01)
4,5,6,7(01--)
5,7,13,15(-1-1)
4
X
X
5
X
X
6
X
8
X
X
X
9
X
X
10
X
13
X
X
Note: Don’t include DCs in coverage table; they don’t have covered by the final logic expression!

## Slide 16: Coverage Table (cont.)
rows = prime implicants
columns = ON-set elements
place an "X" if ON-set element is
covered by the prime implicant
If column has a single X, than the
implicant associated with the row
is essential. It must appear in
minimum cover
0,4(0-00)
0,8(-000)
8,9(100-)
8,10(10-0)
9,13(1-01)
4,5,6,7(01--)
5,7,13,15(-1-1)
4
X
X
5
X
X
6
X
8
X
X
X
9
X
X
10
X
13
X
X
0,4(0-00)
0,8(-000)
8,9(100-)
8,10(10-0)
9,13(1-01)
4,5,6,7(01--)
5,7,13,15(-1-1)
4
X
X
5
X
X
6
X
8
X
X
X
9
X
X
10
X
13
X
X
Coverage Chart

## Slide 17: Coverage Table (cont.)
Eliminate all columns covered by
essential primes
0,4(0-00)
0,8(-000)
8,9(100-)
8,10(10-0)
9,13(1-01)
4,5,6,7(01--)
5,7,13,15(-1-1)
4
X
X
5
X
X
6
X
8
X
X
X
9
X
X
10
X
13
X
X

## Slide 18: Coverage Table (cont.)
Eliminate all columns covered by
essential primes
Find minimum set of rows that
cover the remaining columns
0,4(0-00)
0,8(\000)
8,9(100-)
8,10(10-0)
9,13(1-01)
4,5,6,7(01--)
5,7,13,15(-1-1)
4
X
X
5
X
X
6
X
8
X
X
X
9
X
X
10
X
13
X
X
0,4(0-00)
0,8(\000)
8,9(100-)
8,10(10-0)
9,13(1-01)
4,5,6,7(01--)
5,7,13,15(-1-1)
4
X
X
5
X
X
6
X
8
X
X
X
9
X
X
10
X
13
X
X