## Slide 1: Digital Computer Design
Semiconductor Memory

## Slide 2: Semiconductor Memory
One of the main components in a computer system
  random access memory (RAM) or
  read-only memory (ROM)
Can make memory the same as register file but with more capacity
But, we don’t want to do that because
  we want a lot of memory
  we want it very cheap
    make each memory cell as small as possible
Another reason
  we want to use a common data bus for both reading data from, and writing data to the memory
  thus memory circuit should have just one data port

## Slide 3: RAM (1)
A 2n  m RAM chip: (a) logic symbol; (b) operation table

## Slide 4: RAM (2)
There is a set of data lines, Di
and a set of address lines, Ai
The data lines serve for both input and output of data
The location is specified by the address lines
The number of data lines is dependent on memory word length
The number of address lines is dependent on how many locations are in the memory chip
  e.g. a 512-byte memory chip will have eight data lines (8 bits = 1 byte) and nine address lines (29 = 512).

## Slide 5: RAM (3)
In addition to the data and address lines
there are usually two control lines:
  chip enable (CE), and
  write enable (WR)
For memory access (read operation or write operation):
  the active-high CE line must first be asserted to enable the entire chip
  The active-high WR line selects read or write operation
    WR = 0 : read operation
    WR = 1 : write operation
  Some memory chips have both a read enable and a write enable line
    only one line can be asserted at any one time

## Slide 6
The RAM chip does not require a clock signal
read and write memory operations are not synchronized to the global system clock
They are synchronized to CE and WR
read/write operation begins with a valid address on the address lines
followed immediately by the CE line being asserted
Shortly after, valid data must be present on the data lines
Then WR line is pulled low/asserted
Soon data on the data lines is then read from/written into the memory location that is addressed by the address lines.

## Slide 7
Memory timing diagram: (a) write operation; (b) read operation

## Slide 8
Each bit in a static RAM chip is stored in a memory cell
Main component in the cell is a D latch with enable
A tri-state buffer is connected to the output of the D latch so that it can be selectively read from
The Cell enable signal is used to enable the memory cell for both reading and writing
For reading, the Cell enable signal is used to enable the tri-state buffer
For writing, the Cell enable together with the Write enable signals are used to latch the data on the Input line into the cell

## Slide 9
Memory cell: (a) circuit; (b) logic symbol

## Slide 10: A 4  4 SRAM

## Slide 11
Requires sixteen memory cells forming a 4  4 grid
  Each row forms a single storage location
  the number of memory cells in a row determines the bit width of each location
all of the memory cells in a row are enabled with the same address
A decoder is used to decode the address lines, A0 and A1
  In this example, a 2-to-4 decoder is used
The CE signal is for enabling the chip, specifically to enable the read and write functions through the two AND gates
The internal WE signal, asserted when both the CE and WR signals are asserted, is used to assert the Write enables for all of the memory cells

## Slide 12
Data comes in from the external data bus, Di, through the input buffer and to the Input line of each memory cell
  The purpose of using an input buffer for each data line is so that the external signal coming in only needs to drive just one device (the buffer) rather than having to drive several devices (i.e., all of the memory cells in the same column).
The row of memory cells that actually gets written to will depend on the given address
Read operation requires CE to be asserted and WR to be de-asserted
  This will assert the internal RE signal, which in turn will enable the four output tri-state buffers at the bottom of the circuit diagram
Again, the location that is read from is selected by the address lines.

## Slide 13: VHDL Code for a 16 × 4 RAM Chip
The bi-directional data port, D, is declared as BUFFER so that it can be read from and written to
The actual memory content is stored in the variable mem, which is an array of size 16 of type STD_LOGIC_VECTOR

## Slide 15: Larger Memories
In general, there is always a need for larger memories
Because of product availability constraints
we need to construct these larger memories from multiple, smaller memory chips
Larger memory requirements can be for either
  more memory locations
  wider bit widths for each location or
  both.

## Slide 16: More Memory Locations (1)
Want a 1 K  8-bit memory
Have multiple 256  8-bit memory chips
Need four of these 256  8-bit memory chips, since 1 K = 4  256
A 256  8-bit memory chip has eight address lines, since 28 = 256
Need an additional two address lines decoded to enable one of the four chips at a time
Thus we need a total of ten address lines
First eight, A0 to A7, connected, respectively, in common directly to the eight address lines on the four chips
Last two lines, A8 and A9, connected to the address inputs of a 2-to-4 decoder
The four outputs from the decoder are used to assert the chip enable, CE, line of the four memory chips, RAM0 to RAM3

## Slide 17: More Memory Locations (2)
The data lines and the write enable lines are all connected, respectively, in common
The 256-byte memory chip, RAM0, is enabled when the address bits, A8 and A9, are 00
the address range for RAM0 is from 0 to 255 (0000000000 to 0011111111 in binary)
RAM1 is enabled when the address bits, A8 and A9, are 01
the address range for RAM1 is from 256 to 511 (0100000000 to 0111111111 in binary)
address range for RAM2 is from 512 to 767 (1000000000 to 1011111111 in binary)
the address range for RAM3 is from 768 to 1023 (1100000000 to 1111111111 in binary)

## Slide 18: More Memory Locations (3)

## Slide 19: More Memory Locations (4)
To write to memory location 717, which is binary 1011001101,
the Y2 line of the decoder would be asserted, since bits 8 and 9 are “10”
This Y2 line in turn asserts the CE line of the RAM2 chip
the remaining RAM chips are disabled
Finally, within the RAM2 chip that is enabled, location 205, which is binary 11001101 from bits 0 to 7 of the original address, is selected
Location 205 in the third RAM chip is location 717 for the entire memory, since 2  256 + 205 = 717

## Slide 20: Wider Bit-Width (1)
Want wider bit width for each memory location made from smaller ones
For example, we want a memory that is 512 locations × 16-bits wide from 256 × 8-bit memory chips
Again, we need four 256-byte memory chips

## Slide 21: Wider Bit-Width (2)
For 512 locations, we need two-by-two array of 256-byte chips
  Nine address lines are needed
    First eight, A0 to A7, connected, respectively, in common directly to the eight address lines on the four chips
    A8 is connected to the address input of a 1-to-2 decoder
For a 16-bit wide data bus, we need to connect two 8-bit wide chips in parallel
  each two similar 8-bit wide location in the two chips can be combined together to form a 16-bit wide location
  Since the two chips need to work together, their chip enable, CE, lines must be connected in common and asserted by the same output from the decoder

## Slide 22: Wider Bit-Width (3)

## Slide 23: Wider Bit-Width (4)
Memory chips RAM0 and RAM2 are for storing the data bits D0 to D7
Memory chips RAM1 and RAM3 are for storing the data bits D8 to D15
The address range for RAM0 and RAM1 is from 0 to 255 (000000000 to 011111111 in binary)
The address range for RAM2 and RAM3 is from 256 to 511 (100000000 to 111111111 in binary)