## Slide 1: Digital Computer Design
Sequencing and Control

## Slide 2: Topics
Control unit
  Multiplier as example
hardwired control
microprogrammed control

## Slide 3: Control Units
Two types
  Programmable
  Non-programmable
Look at non-programmable first
  A multiplier

## Slide 4: Algorithmic State Machines
Like a flowchart to express hardware algorithms
ASM describes sequence of events and timing relationships
Can then turn automatically into circuit

## Slide 5: Components (3 of them)
State box specifies a state
  And what register ops and/or outputs happen when in this state

## Slide 6: Decision Box
Based on a single variable
Paths for 0 and 1

## Slide 7: Conditional Output
Register operation is executed if box is reached after decision

## Slide 8: Example
Somewhat like start of CPU

## Slide 9: ASM Block
Another example
Machine idle until START
Then A set to 0
Decision based on Q0

## Slide 10: Timing
States change at clock (this is posedge clocked)

## Slide 11: Example: Binary Multiplier
Two versions
  Hardwired control
  Microprogrammed
Multiplies two unsigned binary numbers

## Slide 12: Multiplication Algorithm
Either select multiplicand or zero
Shift left one every time
Sum all to get product
Result size 2n

## Slide 13: Hardware-Friendly Variation
Partial product
Right shift
Only n bit adder instead of 2n
Each step either add/shift or just shift

## Slide 14: Datapath
Counter size – ceiling of log n
Holds multiplier as well as shifted result. How?

## Slide 15: More
Counter preset to n-1. Counts down.
Signals when it hits zero.

## Slide 16: ASM Chart
Look at it in parts

## Slide 17: Idle
Wait until G asserted
Then clear C and A, and set P to n-1
Then multiplication begins

## Slide 18: Multiplication
Test Q0
  If 1, add B
Recall that MUL1 done all at same time
  What happens to C?
Test counter zero
To IDLE

## Slide 19: Hardwired Control
Two aspects to control
Control of the microoperations
  Generating signals, such as those for the ALU operations, register numbers, etc.
Sequencing
  What happens next?
  The order of any microoperations

## Slide 20: Create Control Sig from ASM
Can look at it one set at a time

## Slide 21: Register A
All microops on Reg A
Last column is combinational expression that controls microop
Name is just assigned by designer

## Slide 22: Register B
LOADB is not listed on ASM chart
It’s an external signal that commands reg to load

## Slide 23: Flip-Flop C
Why is Load repeated?

## Slide 24: Register Q
Similar
  External load
  Shift same as for Reg A

## Slide 25: Counter P
Both of counter’s Ops happen with others, so no new signals

## Slide 26: Sequencing
Now can look purely at sequencing
Only decisions affecting next state are left
  Q0 did not affect next state

## Slide 27: What We Need to Do
Have decided how to generate control signals
Have separated control from timing
Now: implement in logic

## Slide 28: Sequence Register and Decoder
Make register with enough bits to represent states
Add decoder to generate signal for each state
For our example (3 states) need
  2-bit register
  2-to-4 decoder (only need 3 lines of it)

## Slide 29: State Table
Let’s recall how this works by stepping through

## Slide 30: Generate Signals Using Tables

## Slide 31: Circuit

## Slide 32: One-Hot Encoding
One Flip-Flop per state
  Only one of the FFs has value 1
  The single 1 propagates, controlled by combinational logic
Seems wasteful at first glance
  Need n FFs instead of log n
However, it’s easy to design

## Slide 33: Design from ASM
Just use transformation rules to convert ASM to logic
Here’s state box

## Slide 34: Decision Box
Represents both possibilities

## Slide 35: Junction
Junction just an OR gate

## Slide 36: Conditional Output
The action is triggered by the generated control line

## Slide 37: Circuit from Chart
FFs labeled 1, decisions 2, junctions 3, control 4

## Slide 38: VHDL Version
Case statement for sequence of states
  Transition to next state if criteria are true

## Slide 39
_ _Binary Multiplier with n =4: VHDL Description
_ _See Figures 8-6 and 8-7 for block diagram as ASM chart
library ieee;
use ieee. std_logic_1164.all;
use ieee. std_logic_unsigned.all;
entity binary_multiplier is
port (CLK, RESET, G, LOADB, LOADQ: in std_logic;
MULT_IN: in std_logic_vector (3 downto 0);
MULT_OUT: out std_logic_vector (7 downto 0);
end binary_multiplier;

## Slide 40
architecture behavior_4 of binary_multiplier is
type state_type is ( IDLE, MULO. MUL1);
signal state, next_state: state_type;
signal A ,B, Q:std _logic_vector (3 downto 0);
signal P: std_logic_vector ( 1 downto 0);
signal C, Z: std_logic;
begin
Z < = P (1) NOR P (0);
MULT_OUT <= A & Q;

## Slide 41
state_register: process ( CLK, RESET)
begin
if (RESET = ‘1’) then
state < = IDLE;
elsif (CLK’event and CLK = ’1’) then
state < = next_state;
end if;
end process;

## Slide 42
next_state Pfunc: process ( G, Z, state)
begin
case state is
when IDLE =>
if G = ‘1’ then
next_state < = MUL0 ;
else
next_state <= IDLE;
end if;
when MUL0 =>
next _state <= MUL1;
when MUL1 =>
if Z = ‘1’ then
next _state < = IDLE;
else
next_state < = MUL0;
end if;
end case;
end process;

## Slide 43
datapath_func: process (CLK)
variable CA: std_ logic_vector (4 downto 0);
begin
if ( CLK’event and CLK = ‘1’) then
if LOADB = ‘1’ then
B < = MULT_IN;
end if;
if LOADQ = ‘1’ then
Q < = MULT_IN;
end if;

## Slide 44
case state is
when IDLE =>
if G = ‘1’ then
C< = ‘0’;
A< = “0000”;
P < = “11”;
end if;

## Slide 45
when MUL0 = >
if Q (0) ‘1’ then
CA : = ( ‘0’ & A ) + (‘0 & B) ;
else
CA : = C & A;
end if;
C <= CA (4);
A <= CA (3 downto 0);

## Slide 46
when MUL1 =>
C < = ‘0’ ;
A < = C & A (3 downto 1);
Q < =A (0) & Q (3 downto 1);
P < = P – “01”;
end case;
end if;
end process;
end behavior_4;

## Slide 47: This Set of Slides
We’ve taken an example
Created the ASM
Divided into control and sequencing
  Looked at two ways to implement using logic
  Looked at VHDL example
Next
  Look at microprogrammed control of multiplier

## Slide 48: Microprogrammed Approach
Control values stored in a memory
Job of instructions is to generate control signals to datapath and output

## Slide 49: Nomenclature and Characteristics
Word of memory called microinstruction
The set of instructions called microprogram
Sometimes in ROM, sometimes loadable
Often wide word

## Slide 50: Recall Datapath

## Slide 51: Microprogrammed Control Unit
Control Address Register (CAR) equivalent to PC
Sequencer
  Part of instruction sent to next-address generator to determine next instruction addr

## Slide 52: Control Data Register
Pipelining approach to break up the delay in the addr gen and ROM
Not used in example

## Slide 53: Status Bits
Notice that they go only to sequencer
Can only affect next control word
So, conditional output boxes not allowed in this architecture

## Slide 54: ASM – old vs. new

## Slide 55: Microinstruction
Word format
Addresses of potential next instructions
Fields for next instruction selection
Fields for datapath control

## Slide 56: Datapath Control Signals
Doesn’t include load reg inst.
Look at ASM to see where they are asserted

## Slide 57: Mapping to Microinstruction
Have only 4 signals
Could encode (2 bits?)
Would cost a decoder
  Just a design tradeoff
  This design has tiny ROM anyway

## Slide 58: Sequencer Design
Probably most important part of this process
This design provides 2 addrs
  SEL field and control logic choose one
Other possibility is one addr field
  Choice is to go to next sequential addr (like PC), or
  Using control signals go to addr specified

## Slide 59: SEL Field

## Slide 60: Result
5 words in ROM
ROM is 12 bits wide
Design next

## Slide 61: Microprog Design for Mult
Mux chooses addr1 or addr2
Mux control from datapath status and external signals.
Next slide

## Slide 62: Detail of Control

## Slide 63: Microprogram

## Slide 64: Out of Style
Microprogramming less useful now that HLLs used for design
Can use VHDL to generate very complex state machine