## Slide 1: UNIT 3

## Slide 2: UNIT 3 Pollution and Pollution Control
Environmental Crises
Air pollution
Water Pollution
Soil Pollution
Land degradation
Water and wastewater treatment

## Slide 3: Environmental Crises
The laws of energy give keys to understanding the environmental crises currently challenging the world.
Environmental Crisis
Global warming, Ozone layer depletion
Floods Air pollution
Polluted water supply Disease pandemic
Waste disposal Famine
Land degradation Destruction of rainforests
Desertification Rapid population growth etc
Resource depletion
Climate change
Soil pollution

## Slide 4: POLLUTION AND POLLUTION CONTROL
Pollution And Pollutants
Pollution
Undesirable change in the chemical, physical and biological characteristics of air, water and land which tends to harmfully influence life and man and his activities
Pollutants -Any substance that cause pollution
Classified as:
Degradable
Non-degradable

## Slide 5: POLLUTION
Pollution can be defined as an undesirable change in the physical, chemical or biological characteristics of the air, water or land that can harmfully affect health, survival, or activities of humans or other living organisms. Under this definition, pollution does not necessarily have to cause physical harm. It may merely interfere with human activities, e.g. a lake may be considered polluted if it cannot be used for boating activities.
The term ‘undesirable change’, requires value judgements. An alteration may be judged favourable by some; or the undesirable effect may be considered acceptable when compared with the favourable effect e.g. an affluent country may ban the use of DDT as a pesticide because of a judgement that the risks (especially to non-human organisms) outweigh the benefits. At the same time, a country with insufficient food production or a country where malaria affects much of the population may decide that the advantages of using DDT to kill crop pests or malaria-carrying mosquitoes outweigh the risks of its undesirable effects.

## Slide 6: Types of Pollution
Classification of pollutants
One classification of pollutants put pollutants into three divisions.
The first type of pollutants include those substances that occur in
nature, but as a result of human activity are found in unusually large
concentrations e.g. CO2.
The second type of pollutants are the toxic compounds that are released into the environment as a result of anthropogenic activities. These compounds are not found naturally in the environment e.g. mercury, zinc, arsenic, selenium etc.
The third type of pollutants occur when substances which are not
themselves toxic but are released into the environment as a result of
human activity.

## Slide 7: Types of Pollution
Another classification of the pollutants is given based upon the pollutants susceptibility to degradation.
Two Types of pollutants
Degradable Pollutants
Non-degradable Pollutants
Degradable Pollutants
These are the pollutants that can be decomposed, removed,
consumed and thus reduced to acceptable levels either by natural
processes or by human-engineered systems.
Two classes of degradable pollutants
Rapidly degradable pollutants – decomposes faster e.g.
human sewage, animal and crop wastes.
Slowly degradable pollutants – decompose slowly but
eventually are either broken down completely or reduced
to harmless levels, e.g. DDT, radioactive materials
(strontium-90, plutonium-239 etc.).

## Slide 8: Non-degradable Pollutants
These are pollutants not broken down by natural processes. E.g. lead, mercury, some plastics etc.

## Slide 9: Air Pollution
Air pollution refers to the accumulation of substances in the atmosphere that can cause harmful health effects to living things or can negatively affect the public welfare. Negative effects of public welfare include the economic impact or damage to crops or property, such as buildings or works of arts. Air pollution is the result of human activities as well as naturally occurring phenomenon. Transportation, power and heat generation, industrial processes and the burning of solid wastes are the major sources of pollution due to human activities. Volcanic eruptions and naturally occurring fires such as those caused by lightning storms are natural causes of air pollution.
For anyone living in a crowed city it’s hard to envision a world without smog. The word smog is a relatively recent term describing a type of pollution associated with urban settings and smokestack industries. Smog is a blend of the two words smoke and fog and it was first used by the French physician, Dr. H. A. des Voeux.
One of the greatest risk to human health and the environment is air pollution. The list of health problems brought on or aggravated by air pollution includes: lung diseases, such as chronic bronchitis and pulmonary enphysema; cancer, particularly lung cancer; neural disorders including brain damage; bronchial asthma and the common cold which are most persistent in places with highly polluted air and eye irritation.
Environmental problems range from damage to crops and vegetation to acid rain which eventually increases the acidity of some lakes and making them not conducive for the survival of fish and other aquatic life to global warming and destruction of the stratospheric ozone layer which can potentially have devastating effects on our planet.

## Slide 10: Air Pollution
In addition to ozone, common pollutants that were among the first to be regulated throughout the country include: carbon monoxide, airborne particulates, sulfur dioxide, lead, nitrogen oxides, asbestos, beryllium, mercury, vinyl chloride, arsenic, radionuclides, benzene and coke oven emissions.
Carbon monoxide – ordorless gas produced from incomplete combustions
Sulfur dioxide – produced from combustion of coal, fuel oil and diesel fuel.
Nitrogen dioxide – Produced from combustions, motor vehicles, industrial boilers and heaters.
Particulate matter – produced from diesel soot and smoke produced from wood burning. Can also be produced from photochemical reactions among polluting gases, primarily sulfur oxides and nitrogen oxides resulting in corrosive sulfate or nitrate ions.

## Slide 11
Common Air Pollutants | Health concern
Ozone (0.12 ppm) | Respiratory tract problems, asthma, eye irritation, nasal congestion, premature aging of lung tissue
Particulate matter (150 µg/m3) | Eye and throat irritation, bronchitis, lung damage
Carbon monoxide (10 mg/m3) | Cardiovascular, nervous and pulmonary problems,
Sulfur Dioxide (0.03 ppm) | Respiratory tract problems, permanent lung damage
Lead (1.5 µg/m3) | Retardation and brain damage
Nitrogen Dioxide (100 µg/m3) | Respiratory illness and lung damage
Hazardous Air Pollutants | 
Asbestos ( - ) | Variety of lung disease especially lung cancer
Beryllium | Primary lung disease; affects liver, spleen, etc.
Mercury | Damages brain, kidneys and bowels
Vinyl chloride (26 µg/m3)* | Lung and liver cancer
Arsenic | Causes cancer
Radionuclides | Causes cancer
Benzene | Leukemia
Coke Oven Emissions | Respiratory Cancer
Values quoted in the brackets represent the guideline values – California, USA | 

## Slide 12
Air Pollution
A Primary Air Pollutant -Normally defined as a chemical that is added directly to air at harmful concentrations
A Secondary Air Pollutant-Harmful chemical formed in the atmosphere through a chemical reaction among air components

## Slide 13
Air pollution control devices
Natural washout by rain
Catalytic converters
Bag house filters
Cyclone separators
Green House Effects
Warms the atmosphere about 38oC on the average
Enhanced greenhouse effect or global warming is the gradual increase of C02 concentrations in the atmosphere

## Slide 14
Smog
Two types of smog;
Industrial (gray) smog
Photochemical (brown) smog
Effect of air pollution
It causes bronchitis, emphysema, tuberculosis and lung cancer
Unpleasant fumes and dust particles reduce visibility, cause injury to human health and crops and other forms of vegetation.
Air pollutants such as CO, CO2, CH4 causes global warming

## Slide 15
Impacts of atmospheric warming
In 1878, atmospheric warming caused malaria epidemics in North America
100,000 cases of malaria were reported and 28,000 people died
Remedying Green House Effects
Taxing of fuels (which uses carbon) to generate money for the government
Utilise fossil fuels as efficiently as possible
Utilise renewable energy systems

## Slide 16: Green house gases and Global warming
Green house effect is a natural phenomenon caused
predominantly by water vapour, NO2, O3, CO2 and CH4
(methane) and other gases in the atmosphere. Their
effect on the earth is comparable to that of the glass in a
green house. Greenhouse gases greatly affect the
temperature of the Earth; without them, Earth's surface
would be on average about 33 °C (59 °F) colder than at
present.
Control measures
Reduction in fossil fuel use

## Slide 17: Global Warming
Visible light passes through the atmosphere to the earth’s surface.
When the light is absorbed by the earth, it is converted to heat.
Some heat escapes, CO2 and other gases in the troposphere trap the
rest, warming the earth. This allows the earth to maintain a warm
temperature and support life. If there is no green house effect, the
earth will be much colder. In recent years, activities of man have
generated a lot of CO2 and many people have become concerned
about human activity causing the earth to become too warm. It is
important to recognize that there is a great deal of disagreement
among scientists about weather global warming is actually occurring.
Causes of global warming
Certain types of air pollutants may be producing long-term and perhaps irreversible changes to the global atmosphere.
Industrial growth since the mid-nineteenth century has released
large amounts of CO2 into the troposphere.

## Slide 18
Burning fossil fuels such as coal, oil and natural gas also release large amounts of CO2.
Clearing of rain forests by burning the wood contributes CO2 and other green house gases to the atmosphere. Also the clearing means less CO2 is removed from the air by plants.
EFFECTS
Recent studies and computer models indicate that by increasing the amount of CO2 in the atmosphere, we may have initiated a warming trend that may raise, average global temperature between 2°F (-16.7°C) to 8°F (-13.3°C) by the year 2050.
Global warming may change weather patterns and regional climates
Natural important agricultural areas could become less productive
Natural ecosystems would also be affected.
Leads to rising sea levels of one foot in the next 30 to 40 years and two to seven feet by the year 2100. This inundate 50 to 80% of the US, coastal wetlands, erode all recreational beached and increase salinity of estuaries and groundwater.

## Slide 19: Acid Rain
Acid rains is mainly attributable to the strong mineral acids –
Sulphuric and nitric acids that are derived from oxidation of SO2 and
NOx respectively. Pollutant emission of the strong acids - nitric and
sulphuric are slight but atmospheric oxidation NO2 and SO2 causes
formation of these acids. They are removed from the air in rainfall
then known as acid rain (acid fog, acid snow and acid dust). Winds
carry air pollutants hundreds of miles from their points of origin.
These transported air pollutants can damage aquatic ecosystems,
crops and forest and may pose risks to human health. One of the
pollutants is called acid deposition (or more commonly – acid rain).
Acid rain, which results from the reaction of pollutant gases and
moisture in the atmosphere has irreversibly damaged the
environment in many parts of the world. The process of acid
deposition begins with emissions of sulfur dioxide (primarily form coal
burning power plants) and nitrogen oxides (primarily from motor

## Slide 20: Acid Rain
vehicles and coal burning power plants). These
pollutants interact with sunlight and water vapor in the
upper atmosphere to form acidic compounds (sulfuric
acid and nitric acid). These compounds often fall to earth
as acid rain or snow but the compounds can also join
dust or other dry airborne particles and fall as dry deposition.
Effects:
The extent of damage caused by acid rain depends on the total acidity deposited in a particular area and the sensitivity of the area receiving it. Areas with acid neutralising compounds in the soil can experience years of acid deposition without problems.
Since surface waters have less buffering capacity than soils, acid precipitation problems are usually noticed in aquatic ecosystems before they are noticed in terrestrial ecosystems.

## Slide 21: Acid Rain
Acid rain increases acidity of surface waters so much that it reduces or eliminates their ability to sustain aquatic life.
Forest and agricultural crops are vulnerable because acid deposition can leach nutrients from the ground
Can hamper micro-organisms that nourish plants (rhizobium, etc)
Release toxic metals that would normally be tied up in the soil at higher pH.
The pollutants that cause acid rain can also make the air hazy or foggy affecting the enjoyable views of vacationers and potentially affecting communication and navigation.

## Slide 22: Acid Rain
Control:
Power plants burning coal with high sulfur content are considered major cause of acid rain. Coal from e.g. Midwest (U.S.A) has a much higher sulphur content than Western coal. These oxides of N and S released from Midwestern power plants, are carried by winds toward the eastern seaboard and Canada.
Power plants have to reduce release of SO2. Total SO2 released should be permanently limited to the low levels set.
Stiff penalties for plants that release more pollution
Bonus allowance to be given to power plants that install clean coal technology designed to reduce SO2 release or for using renewable energy sources such as solar or wind.
New cars and utility boilers that releases lesser NOx emmissions to be designed.
Solar powered and hydrogen fuel cars

## Slide 23: Water Resources available
Earth hydrosphere=1386million cubic kilometers amount of water
Saline water= 97.5%
Fresh water=2.5%
Ice and permanent snow cover=68.7% of fresh water
Fresh underground water= 29.9%
Total amount of fresh water on earth=0.26%
Notes: Ice and snow cover in Antarctic and Artic and mountainous regions
The amount of fresh water on earth is concentrated in lakes, reservoir and river system
These accessible for economic need and vital for water ecosystem

## Slide 24
Water Pollution
Water pollution is a harmful modification of water caused by the addition of substances likely to modify its quality, aesthetic aspect and use for human purposes. The polluting agent may be physical, chemical or biological in nature and cause discomfort, nuisance or contamination

## Slide 25
Water Pollution
Water has very unusual characteristics, which makes it very ideal for the survival of living things
Dissolves many substances more than any solvent in the world hence it is easily polluted
Major Water Pollutants:
Sewage (waste water from toilets and water from bathrooms and kitchen
Fertiliser
Off shore drilling produce water
Radioactive wastes

## Slide 26
Eutrophication
Over growth of aquatic plants from plant nutrient as a result of pollution
Effects of water pollution
Nuisance and aesthetic insult
Damage to plant and animal life
Human genetic and reproductive damage caused by radioactive, pesticides and industrial chemicals
Property damage caused by muddy and corrosive waters

## Slide 27
Control of water pollution
Treating industrial waste prior to discharge into stream or water bodies
Enacting and enforcing National laws to reduce pollution (EPA guidelines)
Reducing phosphates content in detergent
Oil spills controlled by chemical foams and absorption pads
Research into the finding of oil eating bacteria

## Slide 28
Other Types of Pollution
Thermal Pollution
Noise pollution
Ocean Pollution
Ocean Pollution Threats
Using it as dumping ground for wastes and nuclear testing
Polluting it with oil (oil tankers and oil drilling exploration)
Over exploitation of its resources

## Slide 29: Noise pollution
Noise pollution, unwanted or excessive sound that can have deleterious effects on human health and environmental quality. Noise pollution is commonly generated inside many industrial facilities and some other workplaces, but it also comes from highway, railway, and airplane traffic and from outdoor construction activities.
Mechanical engineers who designed machines and other equipment must produce machines with low noise levels
Noise pollution can also come from churches and funeral grounds
Our studies show that the sound level in many of the churches around KNUST and environs are above 85 decibels the maximum permissible level

## Slide 30
Soil Pollution
Leachates from wastes
Storage of toxic substances
Deliberate injection of wastewater into the soil
Pollution control
Regulation on waste discharges
Prevention of the use of phosphorus in detergents
Prevention bureau
Reduce, reuse, recycle (3Rs)

## Slide 31: Land Pollution
Historically, land has been the recipient of most wastes including those removed from the air and water. Pollution of the land / soil not only threaten the future use of the land but also the quality of the surrounding air, surface water and groundwater. Pollutants on the surface of the land or in the soil frequently move to the surrounding air and water, particularly groundwater. Sometimes this contamination is the result of a direct application, say of pesticides or fertilizers, onto the land; improper storage, handling or disposal of toxic substances.
Industrial waste, if not properly treated and handled can imperil both public health and the environment. Leaks from underground storage tanks and chemical spills also contribute to contamination of the land and groundwater.
If not properly disposed, common household wastes can cause environmental problems ranging from foul-smelling smoke from burning trash to breeding grounds for rats, flies and mosquitoes. Even at properly run disposal sites, land contamination can contribute to air and water pollution because small quantities of toxic substances may be dumped with other household wastes.

## Slide 32: Land Pollution
Rain water seeping through these buried wastes may form leachate. Leachate is the liquid that results when water moves through any non-water media and collects contaminants. Examples would include water as it trickles through either wastes or soils where agricultural pesticides or fertilizers have been applied. This leachate can then percolate down through the soil and may result in contamination of the groundwater.
Other organic wastes such as garbage and paper products decompose and can form explosive methane gas which, because it is lighter than air, tends to rise through the soil and into the atmosphere. Instances of houses near municipal landfills collecting explosive levels of methane gas in crawl spaces or basements have been documented.
The main sources of land pollution are municipal waste disposal, illegal hazardous waste disposal, abandoned hazardous waste sites and underground tanks.

## Slide 34
Ozone
Found in the Stratosphere, hence its name stratospheric ozone
Ozone is a three-atom Oxygen compound
Ozone gas is perceptibly blue in colour and has a characteristic and pungent smell
Occurs between altitudes of 20 and around 35km, normally called the ozone layer
Chloro fluorocarbons causes damage to the ozone layer

## Slide 35: OZONE
The proliferation of ozone is one of the most widespread environmental problems and one of the most difficult to manage. Just about every major urban area of the country exceeds the health protective limits for ozone established by the various EPA. Ozone is a colourless gas with a pungent odour, and the chief component of smog. Chemically it is a form of oxygen with three oxygen atoms instead of the two normally found in oxygen. It is very reactive. Ozone levels high enough to cause health problems for people are also high enough to damage crops and vegetation. Ozone can also damage the lungs of man, building materials and cultural treasures (monuments). Ozone could exist in the troposphere or the stratosphere.
Ozone is produced in the atmosphere (troposphere) when sunlight triggers certain chemical reactions. The precurssors, or chemicals that are initially needed for this reaction to take place include volatile organic compounds (VOCs) and nitrogen oxides (NOx). VOCs are released into the air when petroleum products are combusted, handled or processed. NOx are also produced by combustion. Sunlight provide energy to fuel the reactions between the VOCs and the NOx and naturally occurring atmospheric

## Slide 36
gases, resulting in the production of ozone and eventual generation of smog.
Recent findings indicate that some pollutants especially ozone are more
harmful in lower concentrations than previously thought because they could
life long, permanent health damage. Ozone is the most serious threat
to vegetation. It attacks leaves causing them to yellow, develop dead spots
and drop early. It can reduce plant’s growth, fruit yield and increase
susceptibility to insect attack and interferes with photosynthesis.
OZONE IN STRATOSPHERE
The ozone layer in the stratosphere filters out some of the UV light from the
sun. Destruction of the ozone layer allows more of the sun’s UV rays to
penetrate to us. Increased UV can lead to greater incidence of skin cancer,
Cataracts, reduction in populations of certain fish larvae and plankton. It also
reduces the useful life of outdoor paints and plastics. Chlorofluoro-carbons
(CFC) are compounds that consist of Cl, F and C and used as coolants for
refrigerators, air conditioners, propellants for aerosol sprays agents for
producing plastic foam and cleansers for electrical parts. CFCs do not
degrade easily in the first layer of the atmosphere (troposphere) and so rises
into the stratosphere. CFCs are broken down by UV light in the stratosphere.
The chlorine atoms released react with the ozone layer to convert it into two
molecules of oxygen and chloride.

## Slide 37: Stratospheric Ozone Depletion and anthropogenic enhanced greenhouse effect
Several of the anthropogenic greenhouse gases (e.g. CFCs and N2O) are also ozone depleting gases. Tropospheric warming apparently induces stratospheric colling that exacerbates ozone destruction. As more of Earth’s radiant heat is trapped in the lower atmosphere, the statosphere cools further, enhancing the catalytic destruction of ozone. Further, that loss of ozone itself augments the cooling of the strtosphere. Interactions between climate change and stratospheric ozone may delay recovery of the ozone layer by 15 – 20 years.

## Slide 38
Depletion of the ozone layer will create the following problems:
Human skin cancer
Damage to plant and animal life including food crops
Alteration in global climate patterns

## Slide 39: Wastewater Treatment
Characteristics of Wastewater
Wastewater is commonly used as a synonym for sewage in many places
Sewage consists of black water and grey water. The black water is the one from toilets and the greywater is the one from the kitchen and bath houses
Wastewater contain waste components that impede the application of natural functions of water thus calling for removal of the pollutants before usage
Domestic Wastewater differ from industries and these vary widely in characteristics and composition.
Wastewater contains harmful bacterial and chemicals depending on what the water was used for.

## Slide 40
Types of sewage
Domestic sewage: consist of black water and grey water from toilets and bathrooms respectively. In Ghana grey and black water are separated unlike the developing countries where the wastewater is combined.
Industrial sewage: Include wastes from Tanneries, Canneries, and Pharmaceutical, Textile wastes and beverage industries like the breweries
Municipal sewage: Domestic sewage and waste from public places
Mode of collection
Sewerage system is a network of pipes carrying the sewage from homes to a central treatment plant. This can be very costly. In Ghana and Dubai, the sewage is partially treated in septic tanks and carried by trucks to faecal sludge treatment plants

## Slide 41
Wastewater Treatment
Wastewater has to be treated to reduce the level of pollutants
To encourage re-use and recycle of resources present in wastewater
Treatment plants for this normally consist of :
Primary treatment:
screens
grit chamber
sedimentation tank

## Slide 42
Secondary treatment:
Activated sludge process
Trickling filter process
Waste stabilisation ponds
Tertiary treatment :
Removal of nitrates and phosphates
Advanced treatment:
Recommended when there are other pollutants, which could not be removed during the first three treatment processes

## Slide 43
Wastewater Treatment Technologies
Conventional is when energy for treatment is high cost
Non-conventional or low-cost treatment systemsuses natural treatment such as dependant on sunlight and aquatic plants
Appropriate Technology Selection for Wastewater Re-Use
Wastewater can be used for agricultural purposes, biogas production and aquaculture
In Ghana, the practice of using raw sewage for irrigation is popular with some farmers
Harvesting of fish from the maturation ponds of waste stabilization ponds is also common

## Slide 44
Wastewater Treatment
Wastewater has to be treated to reduce the level of pollutants
To encourage re-use and recycle of resources present in wastewater
Treatment plants for this normally consist of :
Primary treatment:
screens
grit chamber
sedimentation tank

## Slide 45
Pathogens in wastewater
Are disease-causing organisms, in plants, animals and human beings
categorized in five major groups viz: viruses, bacteria, protozoa, fungi and helminths
Infective Dose for Pathogens
Infective doses of pathogens range from one for viruses to several millions for bacteria
Generally, infective doses for viruses and worms are smaller in number than that for bacteria

## Slide 46
Wastewater treatment by algal-based ponds
Combines the primary, secondary and tertiary treatment stages of wastewater treatment in one system
System essentially consists of :
anaerobic,
facultative and
maturation ponds operating in series
Facultative and maturation ponds may be incorporated in the design based on:
Strength of the wastewater
Desired effluent quality

## Slide 47
Performance in Pathogen Removal
Algal-based systems are generally considered to be very efficient in the removal of pathogens
Removal in algal ponds has been documented as 100% for several pathogens including:
Vibrio cholerae, causes cholera
Salmonella, causes typhoid
Enteroviruses, causes polio
Entamoeba histolyca, causes diarrhoea
Ascaris and
Taenia species worms which infect human and animal guts

## Slide 48
Wastewater treatment by Macrophyte-Based Ponds
Aquatic plants known as macrophyes are used in treating waste in waste stabilization ponds.
Macrophyte-based ponds are stabilization ponds
The macrophytes or plants float on the surface of the pond containing the wastewater
Main objectives of using aquatic plants in wastewater treatment are nutrient recycling and economic gains
Categories of Water Associated Diseases
This will be treated in detail under UNIT 4

## Slide 49: DISSOLVED OXYGEN purification of water bodies
Biodegradable organic matter, mostly of domestic origin, removes DO. This is because the micro-organisms present in water consume the organics as food (substrate) and utilize oxygen to accomplish respiration. The more the organics present, the larger the demand on oxygen.
Aquatic animals, including organisms in sediment remove DO.
Plants add DO during the day via photosynthesis but remove it at night by respiration. Dying and decaying plants diminish Do.
In summer periods in temperate countries and tropical countries, the increased water temperature reduces DO solubility.
Tributaries draining into or waste water discharging into a river bring their own oxygen supplies that affect DO of the river on mixing.
Low river flows slow the rate of oxygen transfer into the water from the atmosphere.

## Slide 50: Adverse effects of algae
Occurrence of very turbid and coloured water.
Give rise unstable oxygen conditions by photosynthesis and respiration of algae
Can cause overstrained oxygen economy due to degradation of dead algae, leading to anaerobic conditions at the sediment – water interface
Production of organic compound with chelating properties. Other algae can for gels which can clog rapid sand filters
Blue green algae if prevalent are capable of forming toxins.

## Slide 51: Adverse effects of algae especially for the water supply
Increase of coagulant demand
Flotation of flocs in settling basins
Clogging and passage of filter
Bacterial aftergrowth in distribution system
Adverse effects of aquatic weeds
Clogging of intake screens for water supply or hydropower production
High evapo-transpiration
Interferences with transportation
Interference with fisheries:
fish population and harvesting of fish

## Slide 52
Problems involved in getting clean, safe water to people in the developing world
Contamination of water supply
Deteriorating distribution systems
Absence of Sanitary Infrastructure

## Slide 53
WATER SUPPLY AND SANITATION
Essential in the tropical environment since most of the people rely on on-site water supply and sanitation systems
On-site sanitation :E.g.
VIP latrines
Water Requirement
Water is needed for several purposes and at different times
The quality of water that is needed varies according to use and is termed water demand
Affected by the standard of living and the level of technological development at the place

## Slide 54
Water Supply Engineering
Consists of:
Collecting adequate quantity of water from natural sources
Rendering it fit for human consumption or industrial use
Supplying in a protected way to the consumer
Sources of Water
Rainwater
Surface water
Groundwater

## Slide 55
Treatment of Water
Processes involved :
Plain sedimentation,
Aeration,
Coagulation,
Flocculation,
Sedimentation,
Filtration and
Disinfection in that order

## Slide 56
Distribution of Water
Depends on:
Topography
The location of the source
Other considerations
Canals, flumes, tunnels and pressure pipes are employed in water transportation
Water can be supplied by means of either gravity, pumping or a combination of both

## Slide 57
Uses of Water
Domestic use
Agricultural use
Industrial use
Recreation
Power production (hydropower)
Transportation (navigation)

## Slide 58
Water pollution is a harmful modification of water caused by the addition of substances likely to modify its quality, aesthetic aspect and use for human purposes. The polluting agent may be physical, chemical or biological in nature and cause discomfort, nuisance or contamination

## Slide 59
Treatment of Water
Processes involved :
Plain sedimentation,
Aeration,
Coagulation,
Flocculation,
Sedimentation,
Filtration and
Disinfection in that order

## Slide 60
Distribution of Water
Depends on:
Topography
The location of the source
Other considerations
Canals, flumes, tunnels and pressure pipes are employed in water transportation
Water can be supplied by means of either gravity, pumping or a combination of both

## Slide 61
Uses of Water
Domestic use
Agricultural use
Industrial use
Recreation
Power production (hydropower)
Transportation (navigation)

## Slide 62
Solid Waste
Anything considered useless, unwanted or discarded material that is not liquid or gas
The amounts of waste generated vary according to the income group from which it originates
Solid Waste Collection
Consist of 75-80% of the total solid waste budget
Collection vehicles :
Rear loaders,
Side loaders or front loaders

## Slide 63
Treatment and Disposal of solid wastes
Some of the types of disposal sites are:
Open dump
Landfill
Sanitary Landfill
Secured Landfill
Hazardous Effects of Plastics
Plastics are made synthetically from bi products of fossil fuels
Most polymers are considered non-toxic (PVC is an exception)

## Slide 64
Monomers from which polymers are made may be released and may affect human health
Under the influence of light, heat or mechanical pressure polymers can decompose and release hazardous substances

## Slide 65: Problems of solid waste management in Ghana
1. lack of political will to enforce sanitation by laws
Facilities for solid waste collection not available
Lack of solid waste disposal sites
Lack of willingness by some communities to pay for the management services
Cannot afford to pay for services
Government by law is responsible for waste management but commitment has not been to good
Lack of awareness of the citizenry on the health impact of poor solid waste management

## Slide 66: Assignment
Pollution is caused mainly through anthropogenic activities
1. List the contribution you and your community play in making drinking water unwholesome
2.What are the causes of poor solid waste management in your community
3. Ghana should ban plastics like the other countries eg Rwanda and Tanzania. In your opinion what impacts will it have on your life style as a student and as community
How is waste water managed in your community? Describe it.
What environmental effects do you foresee on the air quality and water bodies?